## Slide 1: Storm Surge and Coastal Inundation Causes, Damages, Risks
Y. Peter Sheng and Andrew Condon
pete@coastal.ufl.edu
Civil and Coastal Engineering
University of Florida
Eric Williford
WeatherPredict Consulting, Inc.
October 25, 2010
Hurricane Science and Society Symposium
New Orleans, LA

## Slide 2: Storm Surge
Abnormal rise of water generated by a storm, over and above the predicted astronomical tide
Storm tide is the water level rise due to the combination of storm surge and the astronomical tide
Notes: http://www.nhc.noaa.gov/ssurge/ssurge_overview.shtml

## Slide 3: What Cause Storm Surge?
Wind Stress –
Cyclonic winds from storm push water toward the shore
Atmospheric Pressure –
Storm center features lower atmospheric pressure than surrounding atmosphere
Water is pushed from surrounding high pressure into low pressure creating bulge
Wave Setup and Wave Runup – Wind generated waves break over shallow water, creating extra momentum in the water. The extra momentum (radiation stress) causes wave setup and runup to add to the storm surge and flooding further inland
Coriolis (earth’s rotation) –
Shore-parallel wind can create high water along the shore (on the right), which then propagates along the shore as a coastal wave, causing storm surge and flooding inland
Notes: http://www.nhc.noaa.gov/ssurge/ssurge_overview.shtml

## Slide 4: Factors affecting storm surge
Storm intensity: higher wind speed and lower central pressure create higher surge
Storm size: larger storms have larger wind fetch creating higher surge
Angle of landfall: more head on landfall creates higher surge
Storm forward speed: the faster moving storms lead to higher surge due to speed of forward motion contributing to higher wind speeds
Offshore bottom slope: gentle sloping bottoms (Gulf coasts) produce higher surge, further inland inundation but lower waves

## Slide 5: Storm Surge Classification
Intensity | Winds | Storm Surge
Category 1 | 74 – 95 mph | 4 – 5 ft.
Category 2 | 96 – 110 mph | 6 – 8 ft.
Category 3 | 111 – 130 mph | 9 – 12 ft.
Category 4 | 131 – 155 mph | 13 – 18 ft.
Category 5 | > 155 mph | > 18 ft.
Storm surge is dependent on much more factors than just hurricane wind speed
Currently no storm surge classification system since there are too many variables for a global classification scheme
New Saffir Simpson Hurricane Scale (SSHS) does not have storm surge levels

## Slide 6: Influence of Storm Size Katrina vs. Camille
Katrina
  Category 3 at landfall (130 mph)
  30 mile Rmax
  27.8 feet of surge
  NHC SLOSH Link
Camille
  Category 5 at landfall (160 mph)
  15 mile Rmax
  22.6 feet of surge
  NHC SLOSH Link
Notes: http://www.wunderground.com/hurricane/surge_details.asp?MR=1 ……click the links to show the animations!
Although Katrina was a Cat-3 hurricane vs. Cat-5 Camille, Katrina was twice as large in size, and the track was closer to New Orleans, hence Katrina generated much higher surge inside Lake Pontchatrain and New Orleans.

## Slide 7
>1,600 Lives Lost…
$120 B in Personal and Public
Property Damage…..
50% of New Orleans
population displaced…
>80% now back
Katrina & Rita together caused ~ 217 square miles
of land loss in an already fragile ecosystem…
Hurricane Katrina (2005) Caused Catastrophe
…and Reminded People of the Danger of
Storm Surge and Coastal Flooding
Loved Ones Lost…
IPET (2008)
NAS/NRC (2009)
Notes: Start by presenting the problem. Katrina as a recent example

## Slide 8: Impact of Katrina on Storm Surge Modeling and Flood Mapping
Significant advances in storm surge modeling and flood mapping
Interagency Performance Evaluation Taskforce (IPET) study
National Academies Committee Report on New Orleans Regional Hurricane Protection System
National Academies Committee Report on Improving FEMA Flood Mapping Accuracy – Mapping the Zone
A Regional Storm Surge and Inundation Model Testbed is comparing 4 academic models (ADCIRC, CH3D-SSMS, CMEPS, and FVCOM) with SLOSH for historical storms and inundation maps (http://ioos.coastal.ufl.edu) pete@coastal.ufl.edu

## Slide 9: Quantifying Storm Surge and Flood Risk – MEOW (Maximum Envelope of Water) and MOM (Maximum of Maximum)
MEOW – Category 3 moving northeast at 5 mph at mean tide (each line a different track)
MOM – Category 3
MEOW and MOM do not include:
effects of waves, precipitation, and probabilistic information
Notes: http://www.nhc.noaa.gov/ssurge/ssurge_momOverview.shtml
The MOMs are used widely by coastal counties on Gulf and Atlantic coasts for hurricane evacuation and coastal development planning.
All the MOMs in Florida have just been updated with the latest Lidar topography data.

## Slide 10: Quantifying Surge and Flood Risk: Base Flood Elevation (BFE) and FIRM
BFE = “100-year flood” = The flood having a one percent (1%) chance of being equaled or exceeded in any given year .
BFE is the national standard used by federal agencies for requiring the purchase of flood insurance and regulating new development.
Base Flood Elevations (BFEs) and Flood Zones are typically shown on Flood Insurance Rate Maps (FIRMs) produced by FEMA, e.g., the following for Sanibel Island, FL.
BFE includes the effects of waves, precipitation, and probabilistic information.
Notes: Sanibel Island FIRM – Zones and Elevation listed (Example VE-EL13 is zone VE and Elevation of 13 feet NAVD88)
http://leegis.leegov.com/LeeSpInS/viewer.htm
FEMA is updating coastal FIRMS along Gulf and Atlantic coasts using more advanced storm surge models while including the effect of waves.

## Slide 11: Pinellas County, FL: MOM, BFE, FIRM
Notes: As an example, the Cat-5 MOM of Pinellas County is shown on the upper left corner, the Base Flood Elevation (100-year flood) is shown on the lower left, while the FIRM with flood zones is shown on the right. The newer BFE does include the effect of waves. Flood elevations shown in MOM and BFE are different.

## Slide 12: From IPET (2008)
Flood risk is reduced due to improved levee protection
Notes: As part of the IPET (2008) study, inundation maps of the New Orleans region were produced. These flood maps considered different levels of levee protection: Before Katrina (upper left), June 1, 2007 (upper right), and with 100-year flood protection (lower left). These flood maps offer more useful information than the FEMA flood maps.

## Slide 13
Different flood map types. (A) historical flood map; (B) flood extent map; (C) flood depth map; (D) flood danger map; (E) qualitative risk map; (F) quantitative risk (damage) map

## Slide 14: Assessing Potential Infrastructure Damage due to Storm Surge and Flooding
Storm surge, wave, and flooding can damage structures (buildings, bridges, and levees) due to water depth and hydrostatic and hydrodynamic forces applied to the structure
It is possible to expand the flood maps to predict the affected population, the number of structures affected, the potential economic damage to the structures affected, etc.
Currently no building guidelines for storm surge hazard

## Slide 15: Going Forward – Mitigating High Flood Risk on Gulf and Atlantic Coasts
Continue with storm surge and inundation model verification and improvement
  Include all relevant processes (wind/atm pressure, waves, tides, precipitation, vegetation, levee, erosion)
  Gather more nearshore data of surge, wave, and inundation for model verification
Flood maps need to include effects of:
  Climate change and sea level rise
  Shore erosion
  Levee reliability
Understand and quantify how marshes can be used to mitigate storm surge and flood risk
Improve storm surge and inundation forecasting – ensemble forecasting
Develop building code for storm surge and flood mitigation