## Slide 1
Select the environmentally correct statement
about the Earth’s atmosphere
Greenhouse gases from automobiles are causing global warming
Airborne dust from volcanic explosions is causing global cooling
The contradiction of “a” and “b” is causing global confusion
Modified from GrinningPlanet Cartoons

## Slide 2
Eyes on the Ocean
Hands-on Learning
Chris Simoniello, Ph.D.
simo@marine.usf.edu
Hurricane Education: Teaching Students and the Public, October 25, 2010

## Slide 3: The Big Picture
International Global Earth Observing System of Systems
  Ocean component: the Global Ocean Observing System (GOOS).
GOOS is coordinated by United Nation agencies.
  More than 100 ocean nations participate.
.
The U.S. contribution to GOOS is the U.S. Integrated Ocean Observing System (IOOS).
The Gulf of Mexico Coastal Ocean Observing System is one of 11 regional programs that comprise the IOOS .
IOOS
President Obama recently signed the Public Lands Bill into law. After eight years, there is authorization for the IOOS program!
Notes: The national initiative is called the Integrated Ocean Observing System (IOOS). It is a component of the international effort to create a world-wide ocean network called the Global Ocean Observing System (GOOS). Ocean.US was created by the National Oceanographic Partnership Program to coordinate the development of IOOS.
IOOS includes a major coastal component – Coastal Ocean Observing Systems (COOS) and calls for establishing a series of regional associations for coastal ocean observing systems.
These regional associations are charged with integrating the various ocean observing efforts that are already underway within each region, as well as planning for expanding these systems as needed. These efforts seek to address many of the issues discussed earlier including how to fill gaps in the observation networks and how to address overlaps in the current systems.
The regional efforts are also incorporating end-users into the implementation process and building data delivery systems that can better meet the needs of coastal user communities.

## Slide 4
Regional Planning Document
Budget plan for observing
capacity
Product & Service development
System management
Education and Outreach
http://www.usnfra.org/documents/03.10_RCBooklet_lo-res.pdf
U.S. IOOS Program Overview

## Slide 5: Integration of Existing Sub-systems
Many operational elements
Operated by separate entities
Funded by a variety of sources
To realize maximum benefit, the whole must operate as one-
planned, coordinated and managed as a system
Notes: 5
Mention for computer-based activities-will be pulling data from a variety of sites

## Slide 6
Balancing the “energy” checkbook
3 types of exchange influence how energy moves heat and water around the planet and between ocean, atmosphere, and land:
Heat flux: movement of energy by shortwave (light) and longwave (heat) radiation; plus direct contact between ocean and air (sensible heat-no phase change); and evaporation or condensation (latent heat-change of phase).
Water flux, the balance between evaporation from the sea surface and precipitation back into the ocean.
Momentum flux, the transfer of energy from the wind pushing against the water.
It’s all about FLUX
Notes: This is the reason the foundation of the program is built on physical oceanographic and meteorological information.

## Slide 7: What ocean conditions can be monitored?
Examples:
Physical Ocean Conditions
  Temperature
  Currents
  Waves
  Water Level
Atmospheric Conditions
  Winds
  Pressure
  Fog
Biological/Ecological Conditions
  Nutrients
  Contaminants
  Benthic Habitat
Notes: A wide range of ocean condition variables can be measured using different types of sensors on the observation platforms. The examples shown here represent a fraction of the potential observation variables. The key to developing successful and sustainable coastal ocean observation systems is to implement the most appropriate and cost-effective combinations of platforms and sensors to meet critical user needs.

## Slide 8: How do scientists observe the oceans?
Buoys
Vessels
Satellites
Aircraft
Radar
Others
Notes: The platforms used for collection of the observation data are diverse. They include but are not limited to: fixed platforms, buoys; research and survey vessels; remote sensing from satellites and aircraft; and remote sensing from land, such as radar. Combined, these data can provide observations at varying spatial and temporal resolutions. This diversity provides opportunities for meeting many different end-user requirements.

## Slide 9
GOES antenna
Solar panel
Rain gauge
Beacon
Anemometer
GPS receiver
Solar radiation (short)
Solar radiation (long wave)
Relative humidity & T
Data logger/processor
Barometric pressure
Radar reflector
ADCP module
Buoy = Platform
BreveBuster
[SENSORS]
Notes: ASIMET Air-Sea Interface meteorology

## Slide 10
Notes: Scientists used to study individual species. The current practice is to gain an ecosystem perspective-identifying how organisms interact with the environment on different temporal and spatial scales.

## Slide 11: Value to Society
Tropical Storm Predictions
  Hurricane intensity & tracks ($1M/mile to evacuate!)
  Storm surge
Projecting an oil spill trajectory
Forecasting harbor water levels
  Climate change mitigation, spatial planning
Public Health
  Diseases of marine organisms
  Harmful algal blooms
  Invasive species
Safe and Efficient Marine Operations
  Commercial transportation
  Search and rescue
  National security
Notes: Hurricane evacuations are based on impacts from potential storm surge and cost approximately $1 million per mile. Predications using expert models coupled with real-time observations can significantly improve the accuracy and timeliness of forecasts to be used in making evacuation decisions.
Oil spill response and recovery efforts are highly dependent on ocean conditions, forecasts and potential impacts. Trajectories are projected through models applied to real-time observations and are used in efforts to contain oil spills as well as to mobilize the necessary resources in response to oil spill impacts.
The safe and efficient operations of ships in busy ports and harbors is highly dependent on accurate coastal ocean information. Models utilize combined information about water levels, winds, waves, and currents to provide forecasts that are critical to safe marine operations by harbor pilots and others.
We currently utilize ocean models to meet a variety of user needs. In the future, better observation coverage, more consistent long-term observation data, and new ocean models will combine to greatly expand the possible uses.

## Slide 12: GCOOS GPS Workshops
Enhance the sharing of data, models, and products via the internet.
Professional development programs for the benefit of formal and informal instructors engaged in STEM (science, technology, engineering and mathematics) education.
Elementary to college-level teachers, and outreach and extension personnel from state agencies, aquariums and science centers.
Outreach to these audiences serves as a platform to inform their wider communities about IOOS-related opportunities for professional and vocational careers.
Notes: Workshops attract many-K-gray-not just classroom teachers. Need for pre-service teacher training...a lot of bang for the buck!

## Slide 13: The Scientific Process
For formal and informal education, develop activities that:
  Promote Ocean Literacy
  Promote Climate Literacy
  Demonstrate the Scientific Process

## Slide 15
Maximum sustained surface wind speed curve for Hurricane Ivan. Aircraft observations adjusted for elevation using 90%, 80%, and 80% reduction factors for observations from 700 mb, 850 mb, and 1500 ft, respectively.

## Slide 16
Maximum sustained surface wind speed curve for Hurricane Ivan during peak intensity

## Slide 17
Pressure observations and minimum central pressure curve for Hurricane Ivan

## Slide 18
Source: E. Robert Thieler, Jeff Williams, Erika Hammar-Klose,
Woods Hole Field Center, Woods Hole, MA
Relative risk is quantified based on:
Tidal range, Wave height , Coastal slope, Shoreline change (erosion/accretion), Geomorphology, and Historical rate of relative sea-level rise.
National Assessment of Coastal Vulnerability to Sea Level Rise
Estimates of future global SLR
based on model output of
Wigley and Raper, 1992
15-95 cm by 2100, with a "best
estimate" of 50 cm (I.P.C.C., 1995)

## Slide 19
Sea level rise is more dramatic than the global average along the Gulf Coast.
The Hadley model predicted an average sea-level rise of 21 cm
over next 100 years in the Gulf Coast region
The Canadian model predicted 39.6 to 48.8 cm
Projected negative impacts to coastal ecosystems and the services they provide:
Loss of barrier islands and wetlands that protect coastal communities and ecosystems from storm surges
Reduced fisheries productivity as marshes and grass beds are displaced
Saltwater intrusion into surface and ground water supplies.
http://www.usgcrp.gov/usgcrp/Library/nationalassessment/gulfcoast/gulfcoast-chapter5.pdf
Gulf Coast Regional Climate Change Impact
Assessment, Southern University, Baton Rouge, LA 70813;
National Assessment of Coastal Vulnerability to Sea Level Rise

## Slide 20
Support improved decision making & timely public warnings
Improved action taking
Storm Surge and Hurricane Katrina: Should I evacuate?
Properly forecasting and
displaying storm surge
information makes it
“easier” to decide when to evacuate and by which route evacuation is safest.
…but not as meaningful as local references

## Slide 21: The Future – Coupling Forecast Model Output with Visualization
Advanced Circulation Model Surge Forecast Hurricane Katrina
Biloxi storm surge forecast depiction
Gulfport storm surge forecast depiction
Should I evacuate ?
People need to identify and find relevance in the information

## Slide 22
http://secoora.org/classroom/virtual_hurricane/surge_of_the_storm

## Slide 23: Hurricane Bingo
Central Pressure | Convergence | Knot | Latitude | Low Pressure System
Eye | Fetch | Gale | Gust | Hurricane Warning
Isobars | Data Buoys | Dropsonde | Atmospheric Pressure | Beaufort Wind Scale
Calm | Nautical Mile | Category 4 Hurricane | Subtropical Waters | Thunderstorm
Tropical Cyclone | Tropical Storm | Wind direction | Wind Shift | Atmospheric Pressure

## Slide 24: QUESTIONS?
Does this mean it’s going to be windy today?
Notes: Hybrid Coordinate Ocean Model; WFS Regional Ocean Model System; WFS Finite Volume Coastal Ocean Model

## Slide 25
Estimates of future SLR based on climate model output (Wigley and Raper, 1992) Increase in global sea-level of between 15-95 cm by 2100, with a "best estimate" of 50 cm (I.P.C.C., 1995).
This rate is more than double the rate of eustatic rise for the past century (Douglas, 1997; Peltier and Jiang, 1997).
The first component entails integrating model output such as eustatic, isostatic, and short-term climatic sea-level change estimates in order to assess the potential impacts on the shoreline due to these changes.
The second component involves developing other databases of environmental information, such as:
Relative coastal sediment supply
Episodic events
Hurricane intensity, track, and landfall location
Nor'easter storm intensity data
El Niño-related climate data such as short-term sea-level rise
Human influences (e.g. coastal engineering).
National Assessment of Coastal Vulnerability to Sea Level Rise